| ATC | Consists of the controllers and supporting staff who communicate with the aircrew |
| --- | --- |
| ATC | Stands for air traffic control |
| ATC | They control the aircraft on the ground, in the circuit and approach |
| ATCC | responsible for the safety of aircraft flying between airfields |
| ATCC | Stands for air traffic control centre |
| ATCC | May be located in Air Traffic Control Radar Units (ATCRUs) which may not be situated on airfields |
| Control Tower | May house a Bird Control Unit (BCU) |
| Control Tower | Always in a prominent position in the aircraft manoeuvring area. |
| Airfield Controller | Works in a glass walled control room on the top of the control tower |
| Airfield Controller | They have uninterrupted views of the manoeuvring area |
| Approach Controller | They control aircraft departing the airfield circuit and those making instrument approaches |
| Approach Controller | They may provide a radar service to aircraft in transit through their area of responsibility |
| Runway Controller | Needed on an airfield with a high rate of take-offs and landings |
| Runway Controller | They are in direct contact with the airfield controller and works from a caravan, painted in red and white squares, positioned to the left of the touch-down end of the runway in use |
| Runway Controller | They can refuse aircraft permission to move onto the runway or to take-off or land. |
| Runway Controller | They also control ground vehicles in the runway area |
| RT | Ground-to-air communications are by this method |
| Tele-talk | A system for direct contact with vital offices and sections on the airfield (i.e. between Tower and Station Commander) |
| VHF- | Means -very high frequency |
| UHF | Means – ultra high frequency |
| Helicopter Operating Areas | Identified with a white letter ‘H’, |

| Airfield Hazard Markings | Identified by a three sided solid, mounted on a pole |
| --- | --- |
| Airfield Hazard Markings | Identifies Stationary Hazards |
| Bad Ground | Used on Airfields where taxying on the grass is permitted |
| Bad Ground | Could be indentified by a white canvas ‘V’ marker with red band |
| RADAR | A short pulse of electromagnetic energy is transmitted from an aerial and the receiver ‘listens’ for an echo. |
| RADAR | This determines the aircrafts position, direction of travel and speed |
| Digital resolution direction finding (DRDF) | It receives RT transmissions from an aircraft and displays it on a cathode ray tube as a green line called a ‘trace’ |
| Digital resolution direction finding (DRDF) | Gives the controller the aircrafts bearing from the airfield |
| Instrument Landing system (ILS) | With this system the pilot interprets the signals and does not need any outside assistance. |
| Surveillance Radar | Controller can locate an aircraft and direct it to a position and height near the airfield for visual or runway approach aid. |
| Precision Approach Radar (PRP) | The controller has two screens – one for elevation and the other for azimuth (left and right) |
| Precision Approach Radar (PRP) | They will eventually be replaced by the new ‘replacement PAR’ |
| Airways | They are imaginary tunnels in the air |
| Width of Airways | These are between 10 and 20 nautical miles and have upper and lower height limits |
| Airways | As they approach airfield they slope down to the ground to form airfield zones. |
| Centre Beacons | This consists of a series of radio navigations beacons. which aircraft fly follow |
| Crossing airways | An aircraft can do this providing the base of the airway is above ground level- the aircraft can be flown underneath and no permission is needed |
| Right of way rules | These govern the way aircraft move about the sky so that accidents can be avoided |
| Balloons | All aircraft must give way to these |
| Balloons or gliders | They have the right of way over both powered airships and aircraft |
| airship | They must give way to both gliders and balloons only |
| Powered aircraft | They must give way to balloons, gliders and airships |
| Approaching Head on | If approaching like this they must both move to their right |
| Converging Courses | If approaching like this the left hand aircraft gives way |
| Overtaking | If this is happening the faster aircraft moves to starboard (turning right) |
| Navigation Lights | Most modern aircraft carry one or more of these so that they can be seen easily. |
| Clock Code | You use this to pin-point the location of this aircraft you would use this |
| 12 o clock |  |
| 3 o’clock |  |
| 6 o’clock |  |
| 9 o’clock |  |